WHY DUPLEX?

The DUPLEX brand name is synonymous with dual efficiency and distinguishes a machine that actually has a dual function thereby providing numerous advantages for the best possible floor cleaning.

THE ADVANTAGE OF DUPLEX:

• OFFSET BRUSHES: The machine will clean into corners and up to skirting without leaving brush marks or splashes on vertical surfaces.

• TWO WAY HANDLE: Allows two way operations without lifting or turning.

• DOUBLE WASHING ACTION SYSTEM: The powerful action of two roller-type brushes with opposed rotation at 650 rpm and a surface speed of 5 meter per second, guarantees an efficient mechanical washing action.

• BRUSH DIAMETER: Large diameter brushes give higher surface speeds and reduced working time.

• BRUSH MOUNTING SYSTEM: Eliminates vibration and bouncing. Gives a quick, simple brush change without the problems caused by corroded spindles/axles.

• DUAL DIRT COLLECTION: Two conveyor belts, one for each brush, ensure an extremely efficient pick up system. The dirty solution is thrown by centrifugal force by both brushes into the conveyor belts and then collected in the recovery tank.

• DUAL CLEANING SOLUTION APPLICATION: Two cleaning solution tanks allow each brush to be fed simultaneously with a constant flow of clean solution giving a more even distribution and ensuring and equally efficient operation in each direction.

• LIFT OUT TANKS: The clean water tanks simply lift out of the machine and are not impeded by cables or fixed valves and are extremely easy to clean.

• RECOVERY TANK: The recovery tank is situated in the centre of the machine between the conveyor belts. Dirty solution, hair, grease, fat etc. are efficiently removed by two trimmer blades.

• MOP UP/ MOP DOWN FACILITY: By moving one switch the machine has the facility to scrub down but will not pick up the cleaning solution. This can be thoroughly agitated to ensure maximum penetration. Switch back to the “pick-up” mode and either re-agitates and collects the dirty solution, or by applying clean water through the machine scrub, rinses and dry.

• BALANCED USE: The location of the two clean water tanks, each of equal weight and resisting directly over the brushes, gives perfect balance. The collection tank in the centre of the machine aids the even distribution of weight. The result is a very “operator friendly” machine, extremely easy to use. Older type designed machines with a clean water tank at the front and the recovery tank at the rear must create weight variation across the brushes during the cleaning operation.

• BRUSH REMOVAL: Hollow brushes ensure ease of cleaning and are quickly removed using a standard 6mm. Allan key (supplied) to loosen two screws.

• VERSATILITY: The machine can be used on all types of flooring, from awkward profiled to polishes marble or lounge carpet.

• ELECTRIC POWER:

DUPLEX 340 900 W. (Similar machines 400 W)

DUPLEX 420 1000 W. (Similar machines 550 W)

DUPLEX 620 1900 W. (Similar machines 800 W)

• TANK CAPACITY (Clean solution):

DUPLEX 340 4.2 Litres (similar machines: 1 litre)

DUPLEX 420 6.0 Litres (similar machines: 2 litres)

DUPLEX 620 9.5 Litres (similar machines: 6 litres)

• THEORICAL WORKING SURFACE AREAS:

DUPLEX 340 180 Mq/h

DUPLEX 420 350 Mq/h

DUPLEX 620 550 Mq/h

VARIED USE

• OPTIONAL ALTERNATIVE BRUSHES ALLOW THE MACHINE TO BE USED FOR:

SCRUBBING-DRYING

CARPET CLEANING

EMULSION POLISH STRIPPING

SCARIFYING

BURNISHING

CLEANING & BUFFING

DISINFECTING

DEODORISING

• SEALS OF QUALITY:

IMQ (Italy)

VDE (Germany)

SEV (Switzerland)

BSI (United Kingdom)

CCA-CENELEC Certification Agreement